PCB Specification

Date:	15th June 2011
Company:	SKA SA
Billing Address:	17 Baker St, Rosebank, Johannesburg, South Africa / PO Box 522940, Saxonwold, 2132
Postal Address:	SKA SA, 3rd Floor, The Park, Park Road, Pinelands, 7405, South Africa
Contact:	David George	Email:	david.george@ska.ac.za
		Tel:	+27 11 442 2434
	Philip Gibbs	Email:	philip.gibbs@ska.ac.za
		Tel:	+27 21 506 7363

Board name:	SFP+ Mezzanine Card
Revision:	0
Release:	PRELIM

PCB Details

PCB Specifications:	IPC 6012 Class 2
Finished Board Size:	90 x 107.4 mm
PCB Type:	Multi-layer
Layer Count:	8
Dielectric:	All dielectric layers to be Isola 370HR high temperature laminate
Nominal board Thickness:	1.6mm; tolerance +/-10%
Hole tolerance:	+3mil for vias; +/- 3mil for component holes and slots
Finish:	ENIG
Soldermask:	Green
Silkscreen:	White
Minimum clearance:	4 mil in BGA areas, 6 mil otherwise
Handling rails:	TBD
Panelisation:	TBD

PCB Stackup

Layer	#	Copper (oz)	Dieletric (mil)**	Filename
Pastemask Top		-	-	sfpp.GTP
Silkscreen Top		-	-	sfpp.GTO
Soldermask Top		-	-	sfpp.GTS
Signal Top	1	0.5		sfpp.GTL
			5mil
Ground 1	2	0.5		sfpp.GP1
			8mil
Signal 1	3	0.5		sfpp.G1
			8mil
Power 1	4	0.5		sfpp.GP2
			*
Power 2	5	0.5		sfpp.G2
			8mil
Signal 2	6	0.5		sfpp.GP3
			8mil
Ground 2	7	0.5		sfpp.GP4
			5mil
Signal Bottom	8	0.5		sfpp.GBL
Soldermask Bottom		-	-	sfpp.GBS
Silkscreen Bottom		-	-	sfpp.GBO
Pastemask Bottom		-	-	sfpp.GBP

* Thickness may be adjusted to achieve nominal total thickness previously specified, to satisfy impedance targets and to accommodate manufacturing processes.

Impedance Controlled Traces

All impedance matching to +/- 10%

Microstrip

Layers:	Signal Top (#1), Signal Bottom (#8)
Target Impedance:	50 ohm
Trace thickness:	8 mil